- DH-15* - Deck mounted hand-held drench hose with ½” IPS U.S. made ball valve, push down valve activation, aluminum mounting bracket, insulator handle, nylon deck flange and locator guide, and 8ft. PVC hose.  Unit shall have polypropylene ‘FS Plus’ spray head with integral “flip-top” dust cover, filter and 3.2-GPM flow control orifice angled at 90°.  Unit shall include ANSI compliant sign.

- Performance:  Unit shall be fully factory assembled and hydrostatically tested to meet or exceed ANSI Z358.1 – 2009, and come with a full 2-year warranty.

- Fixture:  Guardian Equipment G5043